## Slide 1
Key Definitions
Two-stage production:
  Semi-finished: raw materials (active ingredient) & excipients in solution → filled primary containers without packaging (product in a form that can be held but not for sale).
  Finished: semi-finished + secondary packaging materials (label, leaflet, box, carton for palletizing) → packaged product for sale.
Two sub-plants: glass & plastic containers.
  Glass: small volumes — the semi-finished product essentially can be held/stored.
  Plastic: large volumes — in practice filling and packaging are done sequentially.
Container type and size (Vial, Ampoule, Bottle, Bag / 2, 5, 10, 20, 50, 100, 200, 500, 1000 ml) determine the format.
Production/packaging work center: a machine or a line of connected machines that must all operate together to receive the product.
Production/Packaging Cycle: the time window in which all formats are used once in the production or packaging work center.
Format Changeover Cycle: the time window for using one format.
Product Changeover Cycle: the time window for producing one product (semi-finished, finished) — campaign.

## Slide 2
Capacity Planning
Rolling 36‑month forecast with binding character for the next 12 months after each review/target‑adjustment period (=3 months). The reporting period is set to 1 month.
During the reporting/review intervals (1 and 3 months), Sales confirms the forecast: for each order or information within the interval, it either reduces forecast quantities (if part of the original forecast) by converting them into orders, or shifts forecast quantities to a later period, or increases/decreases the forecast based on the free production time provided by the plant, market conditions, and new orders received.
On the quarterly review, for the next cycle, we examine which forecast quantities did not convert into orders and which were canceled or postponed.
Production line capacity (actual production shifts): 52 weeks × (planned shifts/week) − (holiday/vacation shifts) − (preventive maintenance shifts) − (qualification shifts) − (pilot shifts) − (shifts reserved for maximum unplanned breakdowns/delays) − (shifts for expected format changes).
Campaign setup / batch changeover times are considered.
Performance Index %: actual (based on prior month shift performance) – minimum (last year) – target – benchmark.
(capacity planning file under development)

## Slide 3
Production Planning & Scheduling
Plastics: there is no possibility to hold semi‑finished stock — schedule the production work center at the same time as the packaging work center, based on actual orders for finished product.
Glass: create semi‑finished stock based on sales forecast, and schedule finished product based on orders.
Production/Packaging Cycle: the period in which all formats are used once in the work center.
  Plastics: 6 weeks.
  Glass: production 12 weeks / packaging 6 weeks.
Format changeover time:
  Minimum: 1 production campaign (168 hours) (1 week) or 10 days on some lines → same active ingredient / same format.
  Integer number of campaigns/weeks — if the period orders are not enough to fill a production or packaging week, we produce/package orders up to 6 months ahead to meet the minimum changeover time. If that still does not cover the week, we extend to 9 months ahead provided the remaining shelf life is at least 75% of the original shelf life (36 months). Only after completing 6‑month/9‑month orders do we change format before the minimum changeover time.
  During the production or packaging cycle, each format is applied only once in the work center, or not at all if there are no period orders.

## Slide 4
Production Planning & Scheduling
Production Cycle
Format change (e.g., work center with 4 formats where all had period orders)
Campaign | Campaign | Campaign | Campaign | Campaign | Campaign | Campaign
Semi‑finished product changeover time in production
Ideal: 1 product in the maximum possible batch size.
Smaller alternative batch sizes ("sub‑batches") are defined based on sterilization cycles.
Glass liquids: target is to cover the campaign with 1 product for 6‑month semi‑finished stock (9 months if 36‑month shelf life) — maximum batches + sub‑batch if needed.
Glass solids: similarly — (9 months if we are >75% of active ingredient shelf life) — if the week cannot be filled, we close the work center.
We purchase as many raw‑material solid batches as needed so that the remainder left when dividing Remainder [<#Batches>×<kg/batch> / <weekly work‑center fill>] is minimal, between the feasible # of batches required for raw‑material needs >3 months and <6 months.
Plastics: target 1 product based on semi‑finished orders for 6 weeks (next cycle) — if the campaign is not completed we extend to 3‑month orders until filled, otherwise a reduced campaign — always an integer number of batches (if orders do not absorb it, we package it into IC).
Semi‑finished product changeover time in packaging
We group orders in each work center first by packing size (×5/×10/×20) and then by semi‑finished product (to reduce the risk of mix‑up in the packaging materials part only).

## Slide 5
Customer–Product–Order Rating
Customer Rating = XYZ
X = A: 100% On Time In Full, B: On Time Not Full, C: Not On Time In Full, D: Not On Time Not Full) → priority
Y = A: Fixed partial orders / fixed annual total quantity – fixed partial timing, B: Fixed annual total quantity – no fixed timing, C: No fixed annual quantity – fixed timing, D: No fixed quantity – no fixed time) → purchasing strategy
Z = Customer/Product profitability: top 25% (A) / 50% (B) / 75% (C) / 100% (D) profitability across all products per semi‑finished category
Order Rating = n + XYZ
n = 0 when the order is entered into the system; the order slot(s) has default number 1. If the delivery date passes, it automatically becomes 2, and for each packaging cycle it misses the number increases by 1 grade; i.e., if it doesn't enter the next cycle it becomes 3, then 4, etc.
VIP orders (tenders, penalties, etc.) – with Sales Director approval option

## Slide 6
Schedule Definition
We group orders by semi‑finished product (delayed + new + forecast up to 6 months), subtract existing semi‑finished stock, and determine the need for semi‑finished production.
For each semi‑finished product, we sort orders by order importance starting with VIP, then the most delayed (the order importance number). For the same delay level, we continue sorting by customer importance (first rating characteristic) and, within the same first importance characteristic, we sort by customer/product profitability (third importance characteristic).
Based on the capacity plan (machine performance) and the product campaign changeover rule in the production work center, we calculate the required production campaigns by "cutting" the sorted order lists into weeks. If the weeks in the production cycle are sufficient to cover total campaign needs, we proceed with execution based on importance in the order described below:
Between campaigns that include VIP orders, higher profitability (Z characteristic of customer/product rating) comes first. Between weeks with the same delay grade, the X characteristic of customer rating comes first and then Z. Therefore, the placement sequence follows for example: maximum VIP, 2A?A, 2A?B, 2A?C, 2A?D, etc.